## Slide 1
Section 4
Tank Calibration
1) Calibration Using Keypad and X35 Monitor

## Slide 2
CHECK LIST BEFORE YOU FILL TANKS OR START CALIBRATING
1) Check seed plate setting before product is in the metering system you would have empty the metering system to change seed plate setting
2) Check the Collector body diverters, these need to be in CLEAN OUT position for calibrating or you may damage the diverters
3) Make sure you have the hair pins in the correct position for the drive you require on each tank (DIRECT DRIVE OR SLOW SPEED)
4) Make sure you set your GEAR RATIO in your CALIBRATION SCREEN TO 2 for DIRECT DRIVE and SLOW SPEED TO 16

## Slide 3
Before you can Calibrate you need to check a few settings
Seed plate setting what seed plate setting is needed FINE, MEDIUM, COURSE
Which Transmission setting do you need DRIECT DRIVE gear ratio 2 or SLOW SPEED gear ratio 16
SHOWS DIRECT DRIVE HAIR PIN IS OFF THE HYDRUALIC MOTOR
Direct Drive
EXAMPLE:
FINE SEED PLATE SETTING
CANOLA
CANOLA IS A SLOW SPEED SETTING
CANOLA C
FINE
Slow Speed Drive

## Slide 4
From Seeder Controller swipe up from the bottom of your screen and the Control Ribbon will appear
Press Load Global Home Screen Icon

## Slide 5
Press on the CALIBRATION SCREEN

## Slide 6
ICONS THAT YOU WILL USE ON CALIBRATION SCREEN
MANUAL SPEED ON/OFF
SET THE MANUAL SPEED/SHOW SPEED WHEN ON
ENTER CALIBRATION WIZZARD
PRESS TO TOGGLE THROUGH TANKS 1, 2, 3, 4.
PRESS TO SET GEAR RATIO (2 OR 16)
SHOWS CAL FACTOR / UNCALIBRATED/ENTER CAL FACTOR
DIRECT DRIVE =GEAR RATIO 2
SLOW SPEED= GEAR RATIO 16

## Slide 7
PRESS ON MANUAL SPEED WILL TURN GREEN
PRESS ON MANUAL SPEED WHERE THE HAND SPEEDOMETER
KEY PAY WILL APPEAR ENTER YOUR SEEDING SPEED
THEN PRESS GREEN CHECK MARK

## Slide 8
Gear Ratios:
Direct Drive: 2.00 (Cereals / Fertilizers)
Slow Speed: 16.00 (Canola / Inoculants)
PRESS ARROW TO GO TO TANK 2
Direct Drive: 2.00 (Cereals / Fertilizers)
SLOW SPEED DRIVE: 16.00
(Canola, Inoculant)

## Slide 9
1.Ensure Manual Speed is ON and there is a speed showing
2. ENSURE CORRECT GEAR RATIO IS ENTERED 2. Press this ICON and you can enter gear ratio of 2 or 16
Now on with calibration
DIRECT DRIVE =GEAR RATIO 2
SLOW SPEED= GEAR RATIO 16

## Slide 10
Press Multi-Tank Calibration

## Slide 11
PRESS Automatic Calibration
YOU WILL AUTOMATICALY ADVANCE TO GRANULAR CALIBRATION
PRESS THE YELLOW AROW

## Slide 12
PRESS TANK 1 STATE

## Slide 13
AFTER YOU PRESS THE TANK 1 STATE IT WILL TURN GREEN

## Slide 14
USING KEYPAD TO CALIBRATE
PRESS #1 TO ACTIVATE TANK 1
PRESS A TO ACTIVATE CALIBRATION WIZZARD
ON/OFF
RESET
FIRST STEP
SECOND STEP
THIRD STEP

## Slide 15
Allow the metering to run for several rotations, stop the metering by pressing the Stop Key
Remove the sample collector and empty the product back into the tank. This is not a calibration but only to ensure the metering wheels are primed, do not weigh this sample
7.6
Priming the Meter Body

## Slide 16
Clear the priming data by pressing the RESET ICON on the keypad.
After priming the metering wheels you have to empty the calibration box and replace the calibration box back under the tank you are calibrating in this case TANK 1.
YOU CAN PRESS RESET ON THE CALIBRATION SCREEN ALSO

## Slide 17
Turn the metering system ON by pressing the start Key
Caution: The metering will engage and distribute the product into the sample collector
Note: The indicator lights are now Green which confirms that Metering is On and Actively flowing
BEFORE YOUR START YOUR CALIBRATION COMFIRM THAT TANK 1 IS ON AND YOUR IN CALIBRATION
TANK #1 ON GREEN LIGHT
IN CALIBRATION ON GREEN LIGHT
CALIBRATING TANK 1

## Slide 18
The Estimated Weight will count continuously as product is collected into the Sample Collector.
Stop the Metering when the Estimated weight is around 15.00lbs. Proceed with the Yellow Forward Arrow.
PRESS THE STATE ICON TO STOP METERING

## Slide 19
NOW WEIGH THE PRODUCT IN THE CALIBRTION BOX
NOW YOU HAVE WEIGHT YOUR PRODUCT YOU WILL GO BACK TO THE TRACTOR CAB PRESS ON THE YELLOW ARROW
15.25 lbs.

## Slide 20
PRESS ON THE ICON 0.000 lb
KEYPAD WILL APPEAR ENTER ACTUAL WEIGHT
AFTER ENTERING ACTUAL WEIGHT PRESS GREEN CHECK MARK

## Slide 21
ACTUAL WEIGHT ENTED PRESS THE YELLOW ARROW
NOW YOU WILL GO TO THE NEXT SCREEN, PRESS THE Not Saved

## Slide 22
Now Saved
Old cal factor before calibration
NEW CAL FACTOR after calibration
The change was 1.85% difference between old cal factor and the new cal factor
NOW PRESS GREEN CHECK MARK

## Slide 23
Once you press the GREEN CHECK MARK YOU WILL START BACK AT THE CALIBRATION SCREEN. YOU WILL NEED TO PREFORM 2 OR 3 CALIBRATIONS PER TANK WITH THE GOAL BEING TO GET TO LESS THAN 1% FROM YOUR SET RATE