## Slide 1
Map Layers
Section 8
1) Map Layers

## Slide 2
Global Home Screen-Select MAPPING

## Slide 3
For more detail, you can adjust the Map layers to display a real time applied Rate

## Slide 4
Toggle the Coverage Map from Coverage to Applied Rate Map

## Slide 5
You may also toggle between the different Tanks, Press the Green Check Mark

## Slide 6
Press on the Color Band icon a the top of the screen

## Slide 7
Press on the Edit Icon

## Slide 8
Press the Auto Applied icon followed by the Green Check Mark. Repeat the above procedure on the remaining tanks.

## Slide 9
Save the Map layer settings by swiping upwards on the bottom of your screen for the User Control Ribbon and selecting the Change Global Home Sceens Icon

## Slide 10
Press on the middle of Mapping Icon (do not press the small Gears Icon).

## Slide 11
A prompt will be displayed, Do you want to overwrite the Global Home Screen “Mapping”? Yes

## Slide 12
A Keypad will pop up. Name your mapping screen and press the Green Check Mark to confirm the name

## Slide 13
The As applied Data will now be displayed as a multi-colored graph, each color shade represents the lb/ac value. Toggling to the overhead view is a useful method to validate that the application rates have been applied properly. Return to the Map layers icon to select and view the other tanks.